# Measurement report for an excitation emission spectrum

Burner:	C2H2/O2 wt	 (C2H2/O2, H2/O2 welding torch or CH4/air Bunsen burner)

Start-Wavelength:	VIS:	506	 nm	UV:	253

Stop-Wavelength:	VIS:	476	 nm	UV:	238

Step size:	VIS:	0,04	 nm (0,04 nm)	(	UV:	0,02	 nm (0,02 nm)

Loopcount:	751

Location of detection:	laser beam goes through the centre of the flame

total height of flame: 600	 mm

height of interior cone: 100	 mm

height of the laser beam above the torch: 75	 mm

laser beam below the peak of interior cone:  25	 mm

focus of  laser (before) the centre of flame: 40	 mm

focus of VIS: 		focus of UV:

Camera:	flamestar old, 12 bit	 (Flamestar old or Flamestar II FS)

Gain:	9,9

Trigger from laser:	QS-Sync Trigger. High precision trigger

Delay:	5040	 ns	(160 ns)

Width:	30	 ns	(50 ns)

Cooling water:	10	 °C	(10°C to 15°C)

Cooling peltier:	10	 °C	(10°C)

Spectrograph:	100	 l/mm	(100 l/mm or 1200 l/mm)

Centre WL:	397,82	 nm

Range:	189,396	 nm to 606,245 nm   (about 400 nm or 35 nm)

Entrance slit:	100	 µm 	(50µm)

Laser:	485	 mJ/p (450 mJ/p) IR corresponds to      	 mJ/p (200 mJ/p) at 355nm	Lamp voltage: 538	  V

Rep.-Rate:	10	 Hz 	(10 Hz)

Acquisition Timing:	50	 pulses summed	(30 to 50 pulses)

Focus lens:	300	 mm focus length 	(300 mm)

Polrotator:	     	 for VIS (minimum, if no UV; maximum if UV)

min  	 for UV (minimum if UV)

(different E-vector direction of OPO and SHG !)

Mirror:

Spectrum 1:	center	 (e.g. interior cone of the flame)

from line 139	 to line 151

Spectrum 2:	off-center	 (e.g. outer range of flame)

from line 102	 to line 128

Miscellaneous:	Only UV (double prism)

Laser energy not stable during this measurement! Some errors

in the EES

Wavelength check:

Pulse energy: